## Slide 1: Name - Surname: Rabia GÜL Department: Process Design and Product Development Mentor: Ali TIRAK
İstanbul Medipol University Department of Electrical and Electronics Engineering & Biomedical Engineering GPU: 3.35
rabiagul0311@gmail.com
(+90) 533 519 60 68
Notes: Hi everyone! Welcome to my presentation.
Today, I will be presenting you my final project, which is about investigating the role of innocuous pain stimulation in human machine interface enhancement.
Before I start the presentation, I would like to thank my advisor Elif HOCAOGLU and all of the faculty members who support me in this project.

## Slide 2
The presentation planned to be made at the end of the internship could not be presented due to the Corona Virus. For this reason, the presentation slide was prepared by adding the information would be explained orally during the presentation.

## Slide 3
Preparation of the Components
Preparation of the SMD
PCB Cleaning
Assembly of the SMD
Automated Optic Inspection
Selective Soldering
Environmental Test
X-ray Analyzer
Quality Control
Flying Probe Test
Electrical Test
Conformal Coating
During the internship, Printed Circuit Board (PCB) manufacturing process was learned and the devices which are used in this process was examined. A detailed research was done on these devices and the information which are obtained were reported.
Flow diagram of the PCB manufacturing

## Slide 4
PCB Cleaning
Removing resin and flux residues from filled boards and hybrids
Purpose of the PCB Cleaning
Over time, water, dust and dirt can enter your to the devices and accumulate to a point where needed to act to prevent permanent damage to the equipment.
Unwanted material formation causes overheating and component failure.
Before circuit board is cleaned
After circuit board is cleaned

## Slide 5
Assembly of the SMD
Speed Print
 When considered the assembly of the components to the blank printed circuit board (PCB), Liquid solder can be printed on the blank PCB with the help of a sieve in the screen printing machine.
The sieves used while printing and the device used in liquid solder printing is "Speedprint SP700". SP700 series SMT stencil printers are designed for Surface Mount Technology (SMT) production processes.
SMT materials are placed on automatic assembly machines on blank PCB printed with liquid solder.

## Slide 6
Assembly of the SMD
Reflow Oven
Reflow soldering requires a screen process.
In the screen printing process, a paste containing both solder and flux is administered to the PCB solder pads.
To solder the components to the board, a stream of hot air or radiant heat is applied to the whole board.
This evenly heats up the board, the components, and the solder paste, melting the solder in the paste and connecting the components to the board.
The aim of the process is to form solder joints by first pre-heating the components, PCB, solder paste and then melting the solder without causing damage by overheating.
 The components that are mounted in automatic assembly machine are baked to cure the liquid cream on the PCB. "Reflow" and "Vacuum Vapor Phase" oven are used for this process.

## Slide 7
2D/3D Automatic Optic Inspection (AOI)
Limitations of 3D Systems:
Cannot control 2D elements
Significant cost increase
Significant reduction in speed
Height limitation
Shading issues
No color control
AOI is an automatic visual inspection of a PCB where a camera is used to scan the board in extremely fine detail to check for any defects or defects.
AOI is a vital inspection system that allows you to measure and monitor the quality of your PCB production and fix any problem or defect at any strategic point in the process flow.
Pattern matching algorithms keep track of both successful and failed PCB assemblies.
In some cases, implementation, cost factors, and acceptable process parameters may make a 2D machine the better choice, but in other cases the same factors may make a 3D AOI system the better choice.
 After the assembly of the PCB cards is completed and the soldering process is done, an optical inspection is made to check whether the components are correctly mounted to the cards and the soldering is smooth.

## Slide 8
Selective Soldering
SMT packages are more precise and expensive and must be soldered in a reflow furnace. However, some cards still require punched pins. This poses a minor problem because the hollow pins cannot be soldered in a reflow furnace and must be soldered separately. This can be done by hand or with a selective soldering machine.
Selective soldering is used for soldering printed circuit boards assembled with partially or fully perforated components. Selective soldering consists of three steps;
fluxing or liquid flux application,
2) preheating or printed circuit board assembly,
3) soldering with a site-specific soldering nozzle.
 The assembly of the elements that are not SMD material on the card and that need to be soldered manually with a special tool or device is applied by "Selective soldering" or "soldering iron".

## Slide 9
Workspace of Pantograph
Environmental Test Chamber
An environmental test chamber is an enclosed space that essentially recreates conditions to determine how a subject will respond to those simulated conditions. These may include;
extreme heat,
sub-zero temperatures,
relative humidity,
dew point,
wet environments
The environmental chamber can be used to study product performance under a given set of conditions, or to accelerate product lifetime and study the product aging process.
 In order to test the quality of the PCB, materials and cards are subjected to high-speed temperature cycles to reveal possible defects and make the necessary corrections. "Espec" device is used for this process.

## Slide 10
X-ray Analyzer and Quality Control
When it comes to PCB inspection, X-ray is extensively used in the PCB assembly process to test the quality of PCBs, which is one of the most important steps for quality-oriented PCB manufacturers.
 BGA, PGA, the elements whose legs are under the body and the elements with spacers are used at the bottom are checked for solder in the X-ray inspection device. "Phoenix PCBA Analyzer" device is used for this process.
The PCBA analyzer is a high resolution micro focus X-ray system equipped with an open tube from x-ray dedicated to the study of printed circuit board assemblies. Compared to other inspection methods, X-ray can enter the inner packaging and inspect the quality of solder joints.

## Slide 11
Flying Probe Test & Electrical Test
Flying probes are electro-mechanically controlled to access components in printed circuit assemblies. The probes are moved around the tested board using an automatically operated two-axis system, and one or more test probes touch the components of the board or test points on the printed circuit board.
During the electrical test, the functional behavior of the PCB card is followed and examined, and the function test is performed.

## Slide 12
Conformal Coating
 During conformal coating, areas where the card should not be coated are masked. A conformal coating is applied on the card to prevent the card from being affected by the external environment. If the coating is not applied, situations such as oxidation may occur.
The advantages of the conformal coating can be ordered like;
Insulation properties may allow a reduction in PCB conductor spacing
Can help eliminate the need for complex, advanced containment
Ensure a longer service life
Protecting electronic circuits from harsh environments that can include high humidity, various airborne contaminants and varying temperatures
Purpose of the conformal coating

## Slide 13
literature search has been done on what are the s parameters, how are these parameters measured, what is a vector network analyzer how does it work, what is the spectrum analyzer, what are the main differences between these two analyzers

## Slide 14
S parameters

## Slide 15
Measurement of the s parameters

## Slide 16
Vectork network analyzer

## Slide 17
Spectrum analyzer

## Slide 18
Network vs. spectrum

## Slide 19
Tombstone problem

## Slide 20
Vacuum vapor phase soldering

## Slide 21
Unit design – pin to pin mapping

## Slide 22
Thank You for Listening